## Slide 1: First steps with PYNQ-Z2

## Slide 2
Agenda
Configure board, SD card
Connect to the board
Login in to portal
Jupyter Notebook
Labs
  Getting started with Notebooks
  Getting started with IPython
  Exploring PYNQ-Z2
  Programming on-board peripherals

## Slide 3: Prerequisites
PYNQ-Z2 board
SD Card with preloaded Image*
Ethernet Cable
USB cable and available USB port
*Instructions to download and prepare SD card:
http://www.tul.com.tw/download/pynq_z2_v2.2.img.zip

## Slide 4: Pynq overview
Programmable Logic
(Overlay)
Dual Cortex-A9
Pynq
Jupyter
Linux, Jupyter, Pynq
(MicroSD card)
Audio
USB
HDMI In/Out
Pmods
LEDs, Buttons, Switches
Arduino header
Ethernet
Raspberry Pi header

## Slide 5: Connecting to the board
Configure board to boot from SD Card
Insert SD Card
Connect USB cable
Connect Ethernet cable to PC or to a Switch/Router
Power On

## Slide 6: Connecting to the board – Direct connection
Connect board directly to Ethernet port on PC
  USB to Ethernet adapter if no Ethernet port available
Board IP will default to 192.168.2.99
Manually specify static IP for PC
  Must be in same range as board:
    E.g. 192.168.2.1
  No internet access unless you bridge network connections (packages can’t be updated)
Connect board directly to PC

## Slide 7: Connecting to the board – Via network switch
Board is connected to network (switch/router)
  If DHCP server running on network board will get IP from DHCP server
Internet access via network allows Python packages to be installed/updated
PC can connect to same network
  Wired
  WiFi
Connect board to switch/router
PC connected to router via cable or wireless
1
2

## Slide 8: Connecting to the board – Via WiFi
Connect USB WiFi dongle to board
Connect board and PC to wireless hotspot
  Router, Mobile Phone
Need to configure board to connect to WiFi network
  Notebook available to do configuration
    usb_wifi.ipynb
  Manually configure from terminal
    Modify /etc/network/interfaces.d/
    iwconfig in next release
Connect WiFi dongle to board
Connect board and PC to wireless hotspot
1
2

## Slide 9: Configure Ethernet - Windows
Windows 7:
  Control Panel\Network and Internet\Network and Sharing Center
Properties
TCP/IPv4Properties
Set IP address

## Slide 10: Configure Ethernet - Mac
Mac OS:
  Apple menu > System Preferences > Network
  Select interface > Advanced

## Slide 11: Troubleshooting: LEDs, serial connection
Status LEDs
  Power On: Red LED
  Bitstream Loaded (Pynq booting): Green “Done” LED
USB cable provides serial connection to the board
  115200 baud (data:8 bit, stop bits:1)
  Windows: Device manager to get COM port
  Check board has booted
    Is Linux shell available on terminal?
Check/Modify board IP
  ifconfig to check network settings
Modify any other Linux settings
  Proxy, Network settings
  sudo password: xilinx

## Slide 12: Hostname
Linux is running on the board
Change the hostname if multiple boards are on the same network
  Default hostname is pynq
  Linux username:password = xilinx:xilinx
sudo /home/xilinx/scripts/hostname.sh A_UNIQUE_HOSTNAME

## Slide 13: Samba share
Board can also be accessed as a shared drive
  Windows: \\pynq\xilinx
  Linux: smb://pynq/xilinx
  username:password = xilinx:xilinx
Copy files between PC and board
Access documentation/ scripts/Notebooks

## Slide 14: Introduction to Jupyter notebooks
Copy PYNQ_Workshop folder from USB to: \\pynq\xilinx\jupyter_notebooks

## Slide 15: Log in to portal
Open a browser*
  Chrome, Safari, Firefox
Browse to: http://pynq:9090 and log in
  Where pynq is the hostname of the board
  Use the IP address instead of the hostname
username:password = xilinx:xilinx
Browse to PYNQ_Workshop folder
* http://jupyter-notebook.readthedocs.io/en/latest/notebook.html#browser-compatibility

## Slide 16: Lab exercises: Session 1
1 Getting started with Jupyter Notebooks
2 Getting started with IPython
3 Exploring PYNQ-Z2
4 Programming on-board peripherals
Notes: 1从Jupyter笔记本开始
2开始与IPython
3探索PYNQ-Z2
4车载外围设备编程

## Slide 17: Lab Review
Jupyter Notebook
  Web application/server
  Create and share documents
    Live code, equations, visualizations, explanatory text/comments, results
Make a copy of notebook before editing
Sharing Notebooks
  Save the iPython Notebook .ipynb
  Save as… HTML to share results

## Slide 18: Notebook Cells
Code
  Python
Markdown
  Comments and notes
Execute cells to run code/render
Split and reorder cells
Output printed after cell

## Slide 19: Markdown cells
# Headings
* Italics *
** bold **
* Bullet points
* Bullet points
<html></html>
Not just comments. Explanatory text, notes, documentation.

## Slide 20: Shell commands, Cell magics
Execute shell commands directly from notebook
Prefix !
Built in Cell magics

## Slide 21: Help
Command palette: Ctrl + Shift + p keys
Python help:
  Execute “?” In a cell
  Help()
%magic – learn about Ipython magics
  %lsmagic – get list of magics
  %quickref

## Slide 22: Documentation and Support
Documentation
  http://pynq.readthedocs.io
Support
  http://www.pynq.io/support
GitHub
  Issue tracker

## Slide 23: Next steps
examples/
  Peripherals, Grove, Pmod
  How to use overlays
  Other peripherals, PS/PL

## Slide 24: Summary
Configure board, SD Card
Connect to the board
Log In to portal
Jupyter Notebooks
Labs
Help

## Slide 25: Questions?