## Slide 1: Introduction to Overlays

## Slide 2
Agenda
Overlay Concept
Base Overlay
Labs:
  Grove temperature sensor
  Grove light sensor
  Grove ledbar
  OLED
Notes: Overlay 概念与 Base Overlay 相关实验内容，主要为通过Python控制硬件，本次实验选择控制板上资源。

## Slide 3: Overlay Concept

## Slide 4: FPGA overlays – hardware libraries (kernels)
Overlays are generic FPGA designs that target multiple users with new design abstractions and tools
  Post-bitstream programmable via software APIs
  Typically optimized for given application domains
  Encourages the use of open source tools & fast compilation
  Enables productivity from re-using pre-optimized designs
  Exposes benefits of FPGAs to new users
Notes: 覆盖是通用的FPGA设计，针对多个用户，采用新的设计抽象和工具。
基于软件API的后置比特流可编程软件
通常对于给定的应用域进行优化
鼓励使用开源工具和快速编译
利用重复优化设计实现生产率
暴露FPGA对新用户的好处

## Slide 5: FPGA overlays – hardware libraries
Step 1:
Create an FPGA design for a class
of related applications
Step 2:
Export the bitstream and a C API
for programming the design
Step 3:
Wrap the C API to create a Python library
Step 4:
Import the bitstream and the library in your Python scripts and program
Notes: 步骤1：
为一类相关应用创建FPGA设计
步骤2：
导出比特流和用于设计的C API
步骤3：
包装C API创建Python库
步骤4：
在Python脚本和程序中导入比特流和库

## Slide 6: Base Overlay

## Slide 7: Base Overlay (base.bit)
Jupyter Server
Audio
HDMI In/Out
Pmods
LEDs, Buttons, Switches
Arduino header
Tracebuffer
HDMI Out
HDMI In
IOP
Arduino
IOP
IOP
MIC/Audio Out
GPIO Controller
DDR
DDR
Pynq API
Dual Cortex-A9
Interrupt Controller
Tracebuffer
Notes: HDMI输入输出与DDR相连

## Slide 8: Base Overlay – Interface View
Base Overlay is PL design
Standard FPGA design flow
  Vivado IPI
Interface to Python
  Memory Map
Open source
  Components are re-useable
Notes: 基础覆盖是PL设计
标准FPGA设计流程
Vivado IPI
Python接口
内存映射
开放源代码
组件是可重用的

## Slide 9: Pmod IOP
Flexible block allows different peripherals to be used without new hardware design
MicroBlaze processor sharing memory with PS
  IIC, SPI, GPIO, Timer, Interrupt controller, Configurable Switch
Notes: 灵活的块允许在没有新硬件设计的情况下使用不同的外设。
MicroBlaze processor 与PS共享内存
IIC、SPI、GPIO、定时器、中断控制器、可配置交换机

## Slide 10: Arduino IOP
Shared
memory

## Slide 11: Tracebuffer IP
Tracebuffer running at 100 MHz connected to IOP outputs
Stream trace data into DDR memory
  4MB blocks via DMA
64-bit data acquisition
Trigger Conditions
Python control
  Start/stop, Acquisition rate, Number of samples
Notes: Tracebuffer运行在100 MHz连接到IOP输出
流跟踪数据到DDR存储器中
通过DMA的4MB块
64位数据采集
触发条件
蟒蛇控制
开始/停止，获取率，样本数

## Slide 12: Video
HDMI In, HDMI Out
HDMI input controller writes to a framebuffer
  PS DDR memory
  3x framebuffers available
Data path
  Stream from HDMI in to DDR, Stream from DDR to HDMI out
Image processing on PS
  E.g. OpenCV
Notes: HDMI，HDMI输出
HDMI输入控制器写入帧缓冲器
PS-DDR存储器
可用的3X帧缓冲器
数据路径
从HDMI到DDR的流，从DDR流到HDMI输出
基于PS的图像处理
例如OpenCV

## Slide 13: Audio
Audio controller
  MIC in (PDM)
  Line Out (PWM)
Connected to PS in Base Overlay
Notes: 音频控制器
MIN（PDM）
输出线（PWM）
在基础覆盖中连接到PS

## Slide 14: Base Overlay Resource Utilization
Z-7020, Total resource utilization ~50%
  IOP (Pmod) ~ 5% IOP (Arduino) ~ 10%
  Video ~ 10% Audio ~ 2%
  Tracebuffer ~ 3%
Notes: Z-7020，总资源利用率50%
IOP（PMOD）～5% IOP（ARDUINO）～10%
视频~ 10%音频~ 2%
Tracebuffer～3%

## Slide 15: Base Overlay MicroBlaze IOP
ARMA9
ARMA9
AXI-Lite
The A9s control the MicroBlaze processors
They deliver the C code to be executed via dual-ported Instruction BRAMs
They exchange data and control (commands/status) with the MicroBlazes via dual-ported Data BRAMs
Switches
Pushbuttons
LEDs
Onboard (Fixed)
Peripherals
PmodA
PmodB
Arduino
Notes: A9S控制微火焰处理器
它们通过双端口指令BrAMP来执行C代码。
它们通过双端口数据总线交换数据和控制（命令/状态）。

## Slide 16: Pynq_tutorial Overlay

## Slide 17: Pynq_tutorial Overlay (pynq_tutorial.bit)
Jupyter Server
Pmods
Shared LEDs, Buttons, Switches
IOP
IOP
GPIO Controller
DDR
DDR
Pynq API
Dual Cortex-A9
Interrupt Controller
S2MM
FIFO
MM2S
S_AXI_GP1
S_AXI_HP0
S_AXI_HP2
EMIO
EMIO
M_AXI_GP0

## Slide 18: Pynq_tutorial Overlay
Pynq_tutorial Overlay is a light-weight “base” overlay
  IOP1 and IOP2 included
  No Video, Audio, Arduino IOP, Tracebuffer
  MM to Streaming -> FIFO -> Streaming to MM added
  Shared LEDs and buttons between EMIO and MIO ports of PS

## Slide 19: pynq_tutorial Overlay – Interface View
Allows testing of DMA interfaces to AXI streams
  Send and Receive DMAs
Replace FIFO with custom stream IP
Use pynq_tutorial overlay to test DMA operation

## Slide 20: Pynq interface classes
MMIO
  Memory Mapped Input Output
  Register based memory mapped transactions
Xlnk
  Memory allocation (used in DMA)
DMA (drivers)
  Direct Memory Access
  Offload memory transfers from main CPU
GPIO
  Read/Write GPIO wires

## Slide 21: MMIO
Import MMIO
Define memory mapped region
  BASE_ADDRESS: starting location
  ARRAY_SIZE: length of accessible memory
Read and Write 32-bit values
  ADDRESS_OFFSET: Offset from BASE_ADDRESS
  Need to ensure the memory can be read/written
from pynq import MMIO
BASE_ADDRESS = 0x40000000
ARRAY_SIZE = 1024
mmio = MMIO(BASE_ADDRESS, ARRAY_SIZE)
data = 0x12345678
ADDRESS_OFFSET = 0x10
mmio.write(ADDRESS_OFFSET, data)
result = mmio.read(ADDRESS_OFFSET)
print(result)
> 0x12345678

## Slide 22: Xlnk
Memory managed by Linux
  Virtual
Memory must be allocated before it can be accesses by PL
  PL needs the physical address of a memory buffer
Xlnk can allocate (contiguous) memory buffers
  Translates between virtual and physical
  Contiguous memory is more efficient/allows simpler DMA logic
Once buffer is allocated a DMA can be used to transfer data to/from PS/PL
DMA class uses Xlnk for memory allocation

## Slide 23: Xlnk example
Import Xlnk
Allocate contiguous buffer
  cma_alloc()
  Returns Linux virtual address
Get Physical Address
  cma_get_phy_addr()
  Can be used by PL to access DDR (Linux) memory
Write to buffer/Read from buffer
MEMORY_SIZE = 10
from pynq import Xlnk
mmu = Xlnk()
virt_ptr = mmu.cma_alloc(MEMORY_SIZE)
phy_addr = mmu.cma_get_phy_addr(virt_ptr)
buffer = mmu.cma_get_buffer(virt_ptr, MEMORY_SIZE)
buffer = [0,1,2,3,4,5,6,7,8,9]
for i in range(10):
print(buffer[i])

## Slide 24: DMA
Direct memory access
  Transfer data between memories directly
    PS - PL
  Bypasses CPU
    Doesn’t waste CPU cycles on data transfer
  Speed up memory transfers with burst transactions
Xilinx AXI Direct Memory Access IP block supported in PYNQ
  Read and Write Paths from PL to DDR and DDR to PL
  Memory Mapped to Stream
  Stream to Memory Mapped
Needs to stream to/from an allocated memory buffer
  PYNQ DMA class inherits from xlnk for memory allocation

## Slide 25: AXI Direct Memory Access IP
AXI Lite control interface (AXI GP port)
Memory mapped interface (AXI interface, HP/ACP ports)
AXI Stream interface (AXI stream accelerator)
Transfer between streams and memory mapped locations
  Paths from PL to DDR and DDR to PL
  Memory Mapped to Stream/Stream to Memory Mapped
Control interface
(Read)
From Stream to MM
From MM (write)
to Stream
From Stream (write)
to MM
(Read)
From MM to stream

## Slide 26: DMA example
Setup DMAs
Allocate memory buffers
Start DMA transactions
from pynq.drivers import DMA
dma_send = DMA(dma_send_addr, 0) # DMA_TO_DEV
dma_recv = DMA(dma_recv_addr, 1) # DMA_FROM_DEV
dma_send.create_buf(1024)
send_buffer = dma_send.get_buf(32) # 32-bit
send_buffer[i] = …
dma_send.transfer(transfer_size*4, 0) # Bytes
dma_recv.create_buf(1024)
recv_buffer = dma_recv.get_buf(32)
dma_recv.transfer(transfer_size*4, 1)
print(recv_buffer[i])

## Slide 27: GPIO
Up to 64 GPIO wires from PS
  Tri-state
Accessed from Linux
Setup GPIO instance
Map to GPIO pin
  Translated pin numbers to Linux GPIO number
  get_gpio_pin()
Read/Write
Most appropriate for simple control
  Set, reset, start, done …
from pynq import GPIO
btn_gpio = GPIO.get_gpio_pin(0)
led_gpio = GPIO.get_gpio_pin(1)
ps_btn = GPIO(btn_gpio, 'in')
ps_led = GPIO(led_gpio, 'out')
ps_btn.read()
ps_led.write()

## Slide 28: Python Wrapper
Standard Python code
Interface classes used
  MMIO, Xlnk, DMA, GPIO
Check PYNQ repository for examples

## Slide 29: Summary
Overlay Concept
Base Overlay
Pynq_tutorial Overlay
Labs
  GPIO example
  Xlnk example
  DMA example

## Slide 30: Using Sensors

## Slide 31: Load ‘base’overlay on PL
AXI-Lite
Microprocessors
Onboard (Fixed)
Peripherals
Switches
Pushbuttons
LEDs
MicroBlaze
MicroController
MicroBlaze
MicroController
MicroBlaze
MicroController
ARMA9
ARMA9
from pynq import Overlay
ol = Overlay("base.bit")
ol.download()
PmodA
PmodB
Arduino
Python code on ARM A9:

## Slide 32
T
O
I
PMOD
IO1
T
O
I
PMOD
IO2
T
O
I
PMOD
IO8
in(0,7)
out(0,7)
Shared
IBRAM
Shared
DBRAM
CPU
Reset
Switch
IIC(0,2)
CONFIG
GPIO
IIC
SPI(0,3)
SPI
LMB
GPIO
AXI
RESET
ARM
A9
AXI
MicroBlaze
IOP
Code
from pynq import Pmod_OLED, PMODB
oled = Pmod_OLED(PMODB)
oled.write("1 2 3 4 5 6")
Configure IO processor

## Slide 33: Jupyter Notebook
6 lines of user code … thanks to Python, FPGA overlays, abstraction & re-use

## Slide 34: Summary
Overlay Concept
Base Overlay
  Pynq_tutorial Overlay
IOPs
Using Sensors
Labs
  Grove temperature sensor
  Grove light sensor
  Grove LEDBar
  PMOD OLED

## Slide 35: Questions?